## Slide 1: 使用卷積傳遞函數進行聲學傳遞函數半盲估計以應用於去混響 Semi-Blind estimation of acoustic transfer functions with application to dereverberation using convolutive transfer functions Date：2023. 12. 25
Telecom Electroacoustics Audio(TEA) Lab
Presenter:
Anchi Yuan
Notes: Hello everyone
I’m today’s presenter siang. I’m going to share some of my present work in source separation problem. My topic is comparative studies of source separation using semi-blind and blind source separation approaches.

## Slide 2: Outline
Motivation
Literature review
Baseline approach (state-of-the-art BSI method)
Signal model
Flow chart of proposed method
Proposed method
Simulations
Summary
Future work
References

## Slide 3: Motivation
Acoustic transfer functions (ATFs) v.s. Relative transfer functions (RTFs)
Unavailability of the source signal
Most blind system identification (BSI) → multiplication transfer function (MTF)
Proposed method → convolutive transfer function (CTF)
ATF
RTF
Time samples
Magnitude

## Slide 4: Literature review
Higher-order statistics
[1]
Second-order statistics (SOS)
[2]
Subspace (SS) algorithm
[3]
Cross relation (CR) algorithm
[4]
Slow convergence
local minimum
Computatioally intensive
Difficult in adaptive mode
Time domain adaptive eigenvalue decomposition
algorithm (TAEDA)
[5]
Blind system identification (BSI)
Frequency domain adaptive eigenvalue decomposition
algorithm (FAEDA)
[6]
Short RIR

## Slide 5: Baseline approach (state-of-the-art BSI method)

## Slide 6: Signal model
s(n)
a(n)
y(n)

## Slide 7: Flow chart of proposed method
Weighted
prediction
error (WPE)
DAS
beamformer
Three CTF coefficients estimated approach
ATF reconstruction
Parameters optimization
MINT dereverberation
Signal
delay
sDAS,p
or

## Slide 8: Outline of the proposed method
    Wiener filter approach
    RLS approach
    Kalman filter approach
    Pre-processing
    Parameters optimization
    MINT dereverberation
    ATF reconstruction

## Slide 9: Pre-processing of the proposed method
    Extraction of source signal
      WPE for dereverberation
      DAS beamformer for cleaner source

## Slide 10: WPE for dereverberation
    Signal formation
    Algorithm for WPE

## Slide 11: Signal formation
Time samples
C

## Slide 12: Signal formation

## Slide 13: Algorithm for WPE

## Slide 14: DAS beamformer for cleaner source
Rm

## Slide 15: Proposed methods for ATF estimation
    Three CTF coefficients estimated approaches
      Wiener filter approach
      RLS approach
      Kalman filter approach

## Slide 16: Wiener filter approach
Recursive average
yd,p
sDAS,p
Rss,p
Rsy,p
Wiener filtering

## Slide 17: RLS approach
sDAS,p
∑
-
+
yd,p
ep

## Slide 18: Kalman filter approach
Measurement update
(correction)
yd,p
sDAS,p
PKalman,p
No time update (prediction)

## Slide 19: ATF reconstruction
δp
(k)

## Slide 20: Parameters optimization
    Particle swarm optimization (PSO)
      Concept for PSO
      Flowchart for PSO
      Equations for PSO
    A novel hybrid PSO algorithm using an adaptive strategy (ASPSO)
      Flowchart for PSO
      Equations for PSO

## Slide 21: Concept for PSO
      Optimization variable → Initial parameters in three CTF coefficients estimation approaches
      Personal best location & Global best location
      Global exploration ←→ Local exploitation

## Slide 22: Flowchart for PSO
Randomly initialize particle locations X and velocities V
Calculate fitness of particle
Update pbest gbest
Yes
Output gbest
No
Stopping criteia met?
Update particle velocities and locations

## Slide 23: Equations for PSO

## Slide 24: Kalman filter approach
Measurement update
(correction)
yd,p
sDAS,p
PKalman,p
No time update (prediction)

## Slide 25: Flowchart for ASPSO
Randomly initialize particle locations X and velocities V
Calculate fitness of particle
Update pbest gbest
Yes
Output gbest
No
Stopping criteia met?
Update particle velocity
Update inertia weight win
Select Cpbest
Calculate Fpbest
Calculate Mpbest
β < rand?
Update particle position using spiral-shaped mechanism
Update particle position
Replace the particle with the worst fitness
Update pbest
Update gbest
Yes
No
1. Inertia weight with chaotic
2. Elite and dimensional learning strategies
3. Adaptive position update strategy
4. Competitive substitution mechanism

## Slide 26: Equations for ASPSO
1. Inertia weight with chaotic
2. Elite and dimensional learning strategies

## Slide 27: Equations for ASPSO
3. Adaptive position update strategy
4. Competitive substitution mechanism

## Slide 28: MINT dereverberation
    Schematic diagram for MINT
    Algorithm for MINT

## Slide 29: Schematic diagram for MINT
a1(z)
aM(z)
s(n)
a2(z)
.
.
.
w1(z)
wM(z)
w2(z)
.
.
.
ATF in a room
y1(n)
y2(n)
yM(n)
Inverse filter weight

## Slide 30: Algorithm for MINT

## Slide 31: Simulations
    Proposed method v.s. State-of-the-art BSI (short RIR)
    Without Parameters Optimization (long RIR)
    With Parameters Optimization (long RIR)
short RIR
long RIR

## Slide 32: Simulations
    Proposed method v.s. State-of-the-art BSI (short RIR)
    Without Parameters Optimization (long RIR)
    With Parameters Optimization (long RIR)

## Slide 33: Proposed method v.s. State-of-the-art BSI (short RIR)
    Parameters and settings
    RIR estimation results

## Slide 34: Parameters and settings
Uniform linear array (ULA)
Number of microphones = 6
Spacing = 0.03m (3cm)
Aperture = (6-1)*0.03 = 0.15 m
Room size = 0.3m m m
Sampling frequency = 16kHz
Reverberation time T60 = 0.009s (9ms)
Window = 64 samples Hamming window (4 ms) with 75% overlap
Ground-truth RIR : Emanuël Habets, Room Impulse Response Generator
H = 0.3m
W = 0.3m
L = 0.4m
Source
MIC
Small room

## Slide 35: RIR estimation results
Wiener filter approach
Baseline approach
RIR
Absolute error
Frequency (Hz)
Time samples
RIR
Absolute error
Frequency (Hz)
Time samples

## Slide 36: RIR estimation results
RLS
Kalman filter
 | Baseline | Wiener filter | RLS | Kalman filter
ME | 7.33 | 2.65 | 4.90 | 2.17
RIR
Absolute error
Frequency (Hz)
Time samples
RIR
Absolute error
Frequency (Hz)
Time samples

## Slide 37: Simulations
    Compare with state-of-the-art BSI method (short RIR)
    Without Parameters Optimization (long RIR)
    With Parameters Optimization (long RIR)

## Slide 38: Without Parameters Optimization (long RIR)
    Parameters and settings
    RIR estimation results
    MINT dereverberation results

## Slide 39: Parameters and settings
Uniform linear array (ULA)
Number of microphones = 30
Spacing = 0.02m (2cm)
Aperture = (30-1)*0.02 = 0.58 m
Room size = 5m 6m 2.5m
Sampling frequency = 16kHz
Reverberation time T60 = 0.4s to 1.6s with an interval of 0.2s
Window = 1024 samples Hamming window (64 ms) with 75% overlap
Ground-truth RIR : Emanuël Habets, Room Impulse Response Generator
Method to recover source signal : Multiple Input/Output Inverse Theorem (MINT)
Big room

## Slide 40: RIR estimation results
forgetting factor α in Wiener filter | forgetting factor λ in RLS | ε in RLS | η in Kalman filter | ρ in Kalman filter
0.999 | 0.99 | 0.01 | 0.5 | 0.001
Wiener filter with T60 = 0.6s
RIR
Absolute error
Frequency (Hz)
Time samples

## Slide 41: RIR estimation results
RLS with T60 = 0.6s
Kalman filter with T60 = 0.6s
RIR
Absolute error
Frequency (Hz)
Time samples
RIR
Absolute error
Frequency (Hz)
Time samples

## Slide 42: RIR estimation results
T60 (s) method | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6
Wiener filter | 2.86 | 4.76 | 6.05 | 7.66 | 8.83 | 10.26 | 12.37
RLS | 2.91 | 4.87 | 6.98 | 8.46 | 9.30 | 12.12 | 14.63
Kalman filter | 2.86 | 4.76 | 5.97 | 7.64 | 8.90 | 10.37 | 12.43

## Slide 43: MINT dereverberation results
PESQ
SDR (dB)
Perceptual Evaluation of Speech Quality (PESQ)
range: [-0.5 4.5]

## Slide 44: MINT dereverberation results
 | Ground-truth source | Microphone received | WPE+DAS | Wiener filter (MINT) | RLS (MINT) | Kalman filter (MINT)
T60 = 0.6s |  |  |  |  |  | 
T60 = 0.8s |  |  |  |  |  | 
T60 = 1.0s |  |  |  |  |  | 

## Slide 45: Simulations
    Compare with state-of-the-art BSI method (short RIR)
    Without Parameters Optimization (long RIR)
    With Parameters Optimization (long RIR)

## Slide 46: With Parameters Optimization
Method | ME
Kalman filter without parameters optimization | 5.07
Kalman filter with PSO | 4.97
Kalman filter with ASPSO | 4.94
Here, we take η and ρ in Kalman filter as the parameters needed to be optimized.

## Slide 47: Summary
Proposed three approaches
  Accurate ATF estimation
  low matching error
In short reverberation time scenarios
  Proposed method outperform baseline BSI method
In long reverberation time scenarios
  baseline BSI method → failure
  Proposed method outperform WPE following DAS beamformer
Parameters optimization
  Lower matching error

## Slide 48: Future work
Moving sources → Process noise in Kalman non-stationary filter
Real experiments
State-of-the-art BSI → CTF signal model
gm

## Slide 49: References
Y. Sato , “ A method of self-recovering equalization for multilevel amplitude-modulaion IEEE Trans. Commu, vol. 23, no. 6, pp. 679-682, 1975.
L. Tong, G. Xu, and T. Kailath, “A new approach to blind identification and equalization of multipath channels,” Proc. 25th Asilomar Conf. Signals, Syst., Comput, vol. 2, pp. 856–860, 1991.
E. Moulines, P. Duhamel, J. F. Cardoso, and S. Mayrargue, “Subspace methods for the blind identification of multichannel FIR filters,” IEEE Trans. Signal Processing, vol. 43, pp. 516–525, Feb. 1995.
H. Liu, G. Xu, and L. Tong, “A deterministic approach to blind equalization,” Proc. 27th Asilomar Conf. Signals, Syst., Comput, vol. 1, pp. 751–755, 1993.
Y. Huang and J. Benesty, “Adaptive multi-channel least mean square and Newton algorithms for blind channel identification,” Signal Processing, vol. 82, no. 8, pp. 1127–1138, Aug. 2002.
M. A. Haque and M. K. Hasan, “Noise robust multichannel frequency-domain LMS algorithms for blind channel identification,” IEEE Signal Processing Letters, vol. 15, pp. 305–308, 2008.
T. Nakatani, T. Yoshioka, K. Kinoshita, M. Miyoshi and B. -H. Juang, “Speech Dereverberation Based on Variance-Normalized Delayed Linear Prediction,” IEEE Trans. Audio, Speech, Lang. Process., vol. 18, no. 7, pp. 1717–1731, 2010.
Rui ang, Kuangrong Hao, Lei Chen, Tong Wang, and Chunli Jiang, “A novel hybrid particle swarm optimization using adaptive strategy,” Information Sciences, vol. 579, pp. 231-250, 2021.
S. A. U. Islam and D. S. Bernstein, “Recursive Least Squares for Real-Time Implementation,” IEEE Control Systems Magazine, vol. 39, no. 3, pp. 82-85, June 2019.

## Slide 50
© anchi_0203