## Slide 1: 聲學傳遞函數盲估計以應用於去混響、聲源分離以及增強 Blind estimation of acoustic transfer functions with application to signal dereverberation, source separation, and speech enhancement Date：2024. 07. 24
Telecom Electroacoustics Audio(TEA) Lab
Presenter: 袁安志
Research supervisor : 白明憲
Notes: Hello everyone
I’m today’s presenter siang. I’m going to share some of my present work in source separation problem. My topic is comparative studies of source separation using semi-blind and blind source separation approaches.

## Slide 2: Outline
Chapter 1 Introduction
Chapter 2 Baseline approach
Chapter 3 Signal model
Chapter 4 Proposed method
Chapter 5 Simulations
Chapter 6 Experiments
Chapter 7 Conclusions and Future work
References

## Slide 3
Chapter 1 Introduction
  Motivation
  Literature review

## Slide 4: Motivation
Acoustic transfer functions (ATFs) v.s. Relative transfer functions (RTFs)
Unavailability of the source signal
Most blind system identification (BSI) → multiplication transfer function (MTF)
Proposed method → convolutive transfer function (CTF)
ATF
RTF
Time samples
Amplitude

## Slide 5: Literature review
Higher-order statistics
[1]
Second-order statistics (SOS)
[2]
Subspace (SS) algorithm
[3]
Cross relation (CR) algorithm
[4]
Slow convergence
local minimum
Computatioally intensive
Difficult in adaptive mode
Time domain adaptive eigenvalue decomposition
algorithm (TAEDA)
[5]
Blind system identification (BSI)
Frequency domain adaptive eigenvalue decomposition
algorithm (FAEDA)
[6]
Short RIR

## Slide 6
Chapter 2 Baseline approach

## Slide 7: Baseline approach (concept of MCLMS)
Notes: MCLMS: multichannel least mean square

## Slide 8
Chapter 3 Signal model

## Slide 9: Signal model
s(n)
a(n)
y(n)

## Slide 10
Chapter 4 Proposed method
  Flow chart
  TDOA-based source localization
  Pre-processing
  Wiener filter approach
  RLS approach
  Kalman approach
  ATF reconstruction
  Parameters optimization

## Slide 11: Flow chart
Weighted
prediction
error (WPE)
DAS
beamformer
Three CTF coefficients estimated approach
ATF reconstruction
Parameters optimization
Acoustic
applications
Signal
delay
sDAS,p
or
TDOA-based source localization
and mics positions
source position
    Pre-processing
    Parameters optimization
    ATF reconstruction
    Wiener filter approach
    RLS approach
    Kalman filter approach
    TDOA-based source localization

## Slide 12: TDOA-based source localization

## Slide 13: TDOA-based source localization

## Slide 14: TDOA-based source localization

## Slide 15
Pre-processing
  WPE
    Signal formation
    Algorithm for WPE
  DAS Beamformer

## Slide 16: Signal formation
Time samples
D

## Slide 17: Signal formation

## Slide 18: Algorithm for WPE

## Slide 19: DAS beamformer
rm

## Slide 20
Wiener filter approach
RLS approach
Kalman filter approach

## Slide 21: Wiener filter approach
Recursive average
yd,p
sDAS,p
Rss,p
Rsy,p
Wiener filtering
Notes: Minimize mean square error

## Slide 22: RLS approach
sDAS,p
∑
-
+
yd,p
ep

## Slide 23: Kalman filter approach

## Slide 24: ATF reconstruction
δp
(k)

## Slide 25
Parameters optimization
  Which parameter ?
  PSO
    Concept of PSO
    Flow chart of PSO
    Equations of PSO
  ASPSO
    Flow chart of ASPSO

## Slide 26: Which parameter?

## Slide 27: Concept of PSO
      Personal best location & Global best location
      Global exploration ←→ Local exploitation

## Slide 28: Flowchart of PSO
Randomly initialize particle locations X and velocities V
Calculate fitness of particle
Update pbest gbest
Yes
Output gbest
No
Stopping criteia met?
Update particle velocities and locations

## Slide 29: Equations of PSO

## Slide 30: Flowchart of ASPSO
Randomly initialize particle locations X and velocities V
Calculate fitness of particle
Update pbest gbest
Yes
Output gbest
No
Stopping criteia met?
Update particle velocity
Update inertia weight win
Select Cpbest
Calculate Fpbest
Calculate Mpbest
β < rand?
Update particle position using spiral-shaped mechanism
Update particle position
Replace the particle with the worst fitness
Update pbest
Update gbest
Yes
No
1. Inertia weight with chaotic
2. Elite and dimensional learning strategies
3. Adaptive position update strategy
4. Competitive substitution mechanism

## Slide 31
Chapter 5 Simulations
  Fixed source location cases
  Fixed source location with parameters optimization
  Applications of estimated ATFs and RIRs
  Moving source location cases

## Slide 32
Fixed source location cases
  Settings
  Results

## Slide 33: Settings
Hybrid compact-distributed array
Number of microphones in distributed part = 8
Number of microphones in compact part = 30
Spacing of microphones in compact part = 0.02m
Room size = 5m m m
Sampling frequency = 16kHz
Window = 1024 samples Hamming window (64 ms) with 75% overlap
Ground-truth RIR : Emanuël Habets, Room Impulse Response Generator
First mic of ULA

## Slide 34: Results
T60 = 0.01s

## Slide 35: Results
T60 = 1.6s

## Slide 36: Results

## Slide 37
Fixed source location with parameters optimization
  Results

## Slide 38: Results
Method | NRMSPM (dB)
Kalman filter without parameters optimization | -13.2238
Kalman filter with PSO | -13.5870
Kalman filter with ASPSO | -13.5873

## Slide 39
Applications of estimated ATFs and RIRs
  MINT dereverberation
  Settings of TIKR and MPDR
  TIKR source separation results
  MPDR speech enhancement results

## Slide 40: MINT dereverberation
Perceptual Evaluation of Speech Quality (PESQ)
range: [-0.5 4.5]

## Slide 41: MINT dereverberation
 | Ground-truth source | Unprocessed signal | Wiener filter | RLS | Kalman filter
T60 = 0.6s |  |  |  |  | 
T60 = 1.0s |  |  |  |  | 
T60 = 1.6s |  |  |  |  | 

## Slide 42: Settings of TIKR and MPDR
y
x
z
Source 1
Source 2 or interferer
First mic of ULA

## Slide 43: TIKR source separation results
T60 (s) | 0.2 | 0.4 | 0.6
PESQ of source 1 | 3.8347 | 3.6683 | 3.5515
PESQ of unprocessed signal | 1.7486 | 1.5969 | 1.5046
SDR of source 1 (dB) | 26.2406 | 23.4508 | 22.8719
SDR of unprocessed signal (dB) | 4.7966 | 2.4419 | 0.5752
T60 (s) | 0.2 | 0.4 | 0.6
PESQ of source 2 | 2.976 | 2.7389 | 2.7366
PESQ of unprocessed signal | 1.2467 | 1.2444 | 1.219
SDR of source 2 (dB) | 10.5134 | 8.0219 | 9.8436
SDR of unprocessed signal (dB) | -5.3411 | -5.277 | -5.8869
Source 1
Source 2

## Slide 44: TIKR source separation results
 | Ground-truth signal | Unprocessed signal | TIKR separated signal
Source 1 |  |  | 
Source 2 |  |  | 
T60 = 0.6s

## Slide 45: MPDR speech enhancement results
T60 (s) | 0.2 | 0.4 | 0.6
PESQ of enhanced speech signal | 1.8859 | 1.7416 | 1.6923
PESQ of unprocessed signal | 1.7486 | 1.5969 | 1.5046
SDR of enhanced speech signal (dB) | 4.3434 | 3.6316 | 3.2715
SDR of unprocessed signal (dB) | 4.7966 | 2.4419 | 0.5752

## Slide 46: MPDR speech enhancement results
 | Ground-truth source | Unprocessed signal | MPDR enhanced speech signal
T60 = 0.2s |  |  | 
T60 = 0.4s |  |  | 
T60 = 0.6s |  |  | 

## Slide 47
Moving source location cases
  settings
  results

## Slide 48: Settings
First mic of ULA
y
x
z
Moving source
Gap length

## Slide 49: Results
Stationary Kalman filter
Non-stationary Kalman filter
T60 = 0.4s source spacing = 0.3m

## Slide 50: Results
Movement distance (m) | Filter type | NRMSPM1 (dB) | NRMSPM2 (dB) | NRMSPM3 (dB)
0.1 | stationary | -14.3064 | -0.5501 | -0.0847
0.1 | Non-stationary | -14.0583 | -14.4474 | -13.8963
0.3 | stationary | -14.307 | -0.115 | -0.0094
0.3 | Non-stationary | -13.9327 | -14.1249 | -13.4396
T60 = 0.4s

## Slide 51
Chapter 6 Experiments
  Settings and Parameters
  Results

## Slide 52: Settings and Parameters
Hybrid compact-distributed array
Number of microphones in distributed part = 8
Number of microphones in compact part = 6
Spacing of microphones in compact part = 0.07m
Room size = 4m m m
Sampling frequency = 16kHz
Window = 1024 samples Hamming window (64 ms) with 75% overlap
Ground-truth RIR : signal received by a reference microphone
T60 of the room = 0.128s

## Slide 53: Settings and Parameters

## Slide 54: Results
Stationary Kalman filter
MCLMS (baseline)
Method | NRMSPM (dB)
Kalman stationary filter | -2.9109
MCLMS | -0.0013

## Slide 55
Chapter 7 Conclusions and future work
  Conclusions
  Future work

## Slide 56: Conclusions
Proposed three approaches
  Accurate ATF estimation
  lower NRMSPM than MCLMS
Acoustic applications
  Notable improvement in processed signal regarding PESQ and SDR
Parameters optimization
  Getting Lower NRMSPM than the cases without it
Moving source challenge
  Solved by non-stationary Kalman filter

## Slide 57: Future work
Applications in time or MTF domain→ CTF domain
  Reduce the processing time
  Increase the quality of the processed signal
State-of-the-art BSI method → CTF signal model
  Omit source localization procedures

## Slide 58: References
Y. Sato , “ A method of self-recovering equalization for multilevel amplitude-modulaion IEEE Trans. Commu, vol. 23, no. 6, pp. 679-682, 1975.
L. Tong, G. Xu, and T. Kailath, “A new approach to blind identification and equalization of multipath channels,” Proc. 25th Asilomar Conf. Signals, Syst., Comput, vol. 2, pp. 856–860, 1991.
E. Moulines, P. Duhamel, J. F. Cardoso, and S. Mayrargue, “Subspace methods for the blind identification of multichannel FIR filters,” IEEE Trans. Signal Processing, vol. 43, pp. 516–525, Feb. 1995.
H. Liu, G. Xu, and L. Tong, “A deterministic approach to blind equalization,” Proc. 27th Asilomar Conf. Signals, Syst., Comput, vol. 1, pp. 751–755, 1993.
Y. Huang and J. Benesty, “Adaptive multi-channel least mean square and Newton algorithms for blind channel identification,” Signal Processing, vol. 82, no. 8, pp. 1127–1138, Aug. 2002.
M. A. Haque and M. K. Hasan, “Noise robust multichannel frequency-domain LMS algorithms for blind channel identification,” IEEE Signal Processing Letters, vol. 15, pp. 305–308, 2008.
T. Nakatani, T. Yoshioka, K. Kinoshita, M. Miyoshi and B. -H. Juang, “Speech Dereverberation Based on Variance-Normalized Delayed Linear Prediction,” IEEE Trans. Audio, Speech, Lang. Process., vol. 18, no. 7, pp. 1717–1731, 2010.
Rui ang, Kuangrong Hao, Lei Chen, Tong Wang, and Chunli Jiang, “A novel hybrid particle swarm optimization using adaptive strategy,” Information Sciences, vol. 579, pp. 231-250, 2021.
S. A. U. Islam and D. S. Bernstein, “Recursive Least Squares for Real-Time Implementation,” IEEE Control Systems Magazine, vol. 39, no. 3, pp. 82-85, June 2019.

## Slide 59
Q&A

## Slide 60
© anchi_0203

## Slide 61: Equations of ASPSO
1. Inertia weight with chaotic
2. Elite and dimensional learning strategies

## Slide 62: Equations of ASPSO
3. Adaptive position update strategy
4. Competitive substitution mechanism