## Slide 1: Blind estimation of acoustic transfer functions (ATFs) and dereverberation based on convolutive transfer functions (CTFs) Date：2024. 03. 13
Telecom Electroacoustics Audio(TEA) Lab
Presenter:
Anchi Yuan
Notes: Hello everyone
I’m today’s presenter siang. I’m going to share some of my present work in source separation problem. My topic is comparative studies of source separation using semi-blind and blind source separation approaches.

## Slide 2: Outline
Experiment setting
Experiment results
Summary

## Slide 3: Experiment setting
Experiment place : listening room (聆聽室)
Measured reverberation time T60 = 0.17s
Array type : Uniform linear array (ULA)
Number of microphones = 6
Spacing = 0.07m (7cm)
Aperture = (6-1)*0.07 = 0.35m
Sampling frequency = 48kHz
Source type : white noise

## Slide 4: Experiment results (Kalman stationary)
direct sound does not match

## Slide 5: Experiment results (Kalman nonstationary)
direct sound does not match

## Slide 6: Experiment results
Method | NRMSPM(dB)
Kalman stationary | -5.3631
Kalman nonstationary | -5.0719

## Slide 7: Summary
MCLMS of BSI → failure (out of memory)
Mismatch of direct sound → measurement error of distance between mics and loudspeaker